## Slide 1: Regression and Time Series Mixture Approaches to Predict Resilience
Priscila Silva
PhD Candidate
Lance Fiondella
Associate Professor
Technical Meeting
IEEE Boston/Providence/New Hampshire Reliability Chapter
March 2024
Department of Electrical & Computer Engineering
University of Massachusetts Dartmouth

## Slide 2: Objective
In this talk
  Definitions of resilience
  Limitations of resilience metrics
  How to characterize resilience in terms of detrimental and restorative factors
  How to track and predict system resilience
  The benefits of system resilience modeling

## Slide 3: Introduction
System Resilience
  Prepare, absorb, recover, and adapt from failures
  Level of goal achievement
  Applicable to various domains
Constituents
Goal
Domains
Infrastructure
Collaboration
Transparency
Inclusion
Engagement
Communication
Cybersecurity
RESILIENCE

## Slide 4: Motivation
Lack of resilience is dangerous
  Northeast blackout of 2003: software errors
    20% of the electrical service reduced
    45 + 10 million people in the US + CAN affected
    $4 - $10 billion of financial losses
    Mortality rate increased 28%

## Slide 5: Motivation
Lack of resilience is dangerous
  Unemployment rate of 2020 in the US: COVID-19
    22.4 million jobs lost in March of 2020
    Gross Domestic Product decreased 32.9%
    1,134,913 deaths

## Slide 6: Reliability vs. Resilience
Performance
Time
Minimum Performance
Event
Negative Impacts
Start-Point
Normal Functionality
Degraded Functionality
Resilient System
Non-Resilient System
Reliability
Resilience

## Slide 7: Reliability vs. Resilience
How would you measure the reliability and resilience of a power grid?
Reliability: the frequency of power outages
Resilience: how quickly the grid can recover from a blackout

## Slide 8: Reliability vs. Resilience
RESILIENCE
Disaster
Recovery
Reliability
Normal Functionality
Diagnose
Repair
Normal Functionality
MTTF
MTTR
MTTF
MTBF
First
Failure
Second
Failure
Begin
Repair
End
Repair
Data
Lost
Expected
Downtime
RPO
RTO
MTD
First
Failure
Required
Recovery
Expected
Recovery
Second
Failure
Backup
Backup
RPO
Data
Lost
Maintaining continuous operation
Responding to unforeseen events
MTTF: Mean Time to Failure
MTTR: Mean Time to Repair
MTBF: Mean Time Between Failures
RPO: Recovery Point Objective
RTO: Recovery Time Objective
MTD: Maximum Tolerable Downtime

## Slide 9: Resilience Curve
Conceptual resilience curve
Real world disaster management does not look like a textbook curve
Common resilience metric
  Performance Preserved
  Performance Lost
Disaster Resilience: A National Imperative. Washington, D.C.: The National Academies Press, Washington, D.C. (2012).

## Slide 10
System Performance
Performance is domain dependent
  Generalized as the level of goal achievement of task or system
  Performance changes over time
  performance in present time interval
  performance in previous time interval
  change in performance (assumed I.I.D.)

## Slide 11: Resilience Modeling Approaches
Regression Models
  Multiple linear regression (MLR), (MLRI), and (PR)
number of covariates
baseline change in performance
coefficients of disruptions and activities
covariates driving degradation/recovery
number of lags
Modeling change in performance ()
Time Series Models
  Multivariate Vector Auto-Regressive (MVAR), and (MVARMA)

## Slide 12: Mixture Resilience Models
Multiple linear regression and Multivariate Vector Auto-Regressive (MLR-MVAR)
Modeling change in performance ()
MLR-MVARMA
MLRI-MVAR
MLRI-MVARMA
PR-MVAR
PR-MVARMA

## Slide 13: Steps to Apply Resilience Models
  1) Identify disruptive and restorative activities
  2) Collect data for events and activities in each time interval
  3) Estimate model parameters and
    Maximum Likelihood Estimation (MLE)
  4) Validate the model with statistical measures
    How well do the models track the available data (RMSE)?
    How well do the models predicts future intervals (PRMSE)?
    How well do the factors characterize changes in performance ()?
    How much uncertainty is there in the model predictions?

## Slide 14: Illustration: 1980 US Recession – Energy Crisis
  Performance is the number of employments in the US
  Covariates are selected by forward/backward stepwise procedure
Covariates | Description | Covariates | Description
X1 | Treasury Yield Curve | X5 | Personal Consumption Expenditures
X2 | Industrial Production | X6 | S&P 500 Index Stock Market
X3 | Federal Funds Rate | X7 | Consumer Price Index
X4 | Mortgage Rate | X8 | Crude Oil Prices

## Slide 15: Illustration: Computation Steps
  11 Models were tested: 3 regressions, 2 time series, 6 mixture models
            Different combinations of covariates and lags for each approach
  4 data subsets were used for model fitting: 50%, 60%, 70%, 80%
  Model fits and goodness-of-fit were computed
  The best model fit from each approach for each subset considered is plotted against each other for analysis
  The best model fit overall is picked for further analysis

## Slide 17: Illustration: Goodness-of-fit
Model | Covariates | Lags | Parameters | RMSE | PRMSE | 
MLR | X8, X3 | 0 | 3 | 0.00524 | 0.00855 | 0.93122
MVAR | X8, X3, X5 | 4 | 17 | 0.00235 | 0.00240 | 0.92277
PR-MVARMA | X8, X3, X5, X2, X6, X4 | 1 | 21 | 0.00192 | 0.00231 | 0.98628
Model | Covariates | Lags | Parameters | RMSE | PRMSE | 
MLR | X8, X3 | 0 | 3 | 0.00524 | 0.00855 | 0.93122
MVAR | X8, X3, X5 | 4 | 17 | 0.00235 | 0.00240 | 0.92277
PR-MVARMA | X8, X3, X5, X2, X6, X4 | 1 | 21 | 0.00192 | 0.00231 | 0.98628

## Slide 18: Illustration: Best Model Overall
  Polynomial Regression and Multivariate Vector Auto-Regressive Moving Average (PR-MVARMA)

## Slide 19: Illustration: Resilience Metrics
Metrics | Data | MLR | MVAR | PR-MVARMA
Performance Preserved | Actual Predicted Relative Error | 45.8167 45.7127 0.0022 | 45.8167 45.8556 0.0008 | 45.8167 45.8482 0.0006
Performance Lost | Actual Predicted Relative Error | 0.8054 0.8776 0.0896 | 0.8054 0.7718 0.0416 | 0.8054 0.8122 0.0083
  Mixture Models closely approximate actual values of resilience metrics

## Slide 20: Research Questions
    How to
    1) preserve a specified level of performance?
    2) ensure the duration of degraded performance is bounded?
    3) rapidly and cost-effectively recover to a high level of performance?

## Slide 21: Predictive Resilience Assessment Tool (PSRAT) - In development

## Slide 25: Take-Aways
    From this talk, you should be able to
  Distinguish the stages of system resilience
  Identify disruptive events and restorative actions
  Understand the theory of resilience modeling and how it can be used to track and predict system performance
  Apply resilience tools with data
  Select models through statistical inference

## Slide 26: Thank You
                Priscila Silva
                psvila4@umass.edu
    Lance Fiondella
    lfiondella@umassd.edu
                This research is supported by